Evaluating Your Septic System

Homeowner Self-assessment

|  | Septic System Features | Higher Risk (H) | Lower Risk (L) | Indicate with H or L |
| --- | --- | --- | --- | --- |
| 1. | Can you locate your septic tank? | No | Yes |  |
| 2. | Is there a clean out between the house and the septic tank? | No | Yes |  |
| 3. | Can you locate your leach field? | No | Yes |  |
| 4. | What is the distance from the septic system to surface waters? (canals, streams, rivers, etc.) | Less than 100 feet away | More than 500 feet away |  |
| 5. | Does terrain slope towards or away from surface water? | Toward | Away |  |
| 6. | What is the slope of the terrain? | Steep to Moderate | Flat |  |
| 7. | What are the soil types? | Gravelly or rocky soils that water runs easily through or very tight, clayey soils that water cannot penetrate | Medium textured soils that allow water infiltration |  |
| 8. | What is the distance to any water wells? | Less than 100 feet away | More than 500 feet away |  |
| 9. | Is the groundwater from any such well used for human drinking water? | Yes | No |  |
| 10. | Is an impermeable surface such as concrete, asphalt or brick located over the leach field? | Yes | No |  |
| 11. | Trees, large shrubs or other plants with extensive root systems were observed in the vicinity (10 feet) of the leach field? | Yes | No |  |
| 12. | Heavy objects (e.g. cars); or evidence from such objects (e.g. tracks and impressions) are in the vicinity (i.e. directly over) the leach field? | Yes | No |  |
| 13. | Are there one or more of the following signs of system malfunction present? ___ Septic Odors ___ Ponding or wastewater breakout ___ Burnt out grass or ground staining over the leach field ___ Patches of lush green grass over the leach field ___Pipes exposed at or near the ground surface ___Cracks or signs of leakage in risers and lids | Yes | No |  |
| 14. | Stormwater, sump pumps, foundation drains or roof runoff is diverted to flow into the septic system? | Yes | No |  |
| 15. | An apparent cave-in or exposed component was identified? | Yes | No |  |
| 16. | Was the septic system pumped within the last 5 years? | No | Yes |  |
| 17. | Is wastewater discharged through a straight pipe into stream or man-made means of conveyance? (no tank or leach field) | Yes | No |  |
| 18. | Determine the relationship between your septic tank size and the size of your house hold. If you don’t know the size of your septic tank, rank yourself as High. | Adequacy of Septic Tank Size Tank Size Number of Bedrooms 1-3 4 5 <1000 gal H H H 1000 gal L H H 1250 gal L L H 1500 gal L L L |  |

If the response to a specific question falls in between the Higher Risk and Lower Risk categories, please leave the corresponding self-assessment block blank. If after completing the self-assessment you discover the majority of your responses fall into a high risk category, it is recommended that you seek further assistance by contacting the Washakie County Conservation District at 347-2456 ext. 101.  Even if you have marked only a few in the high risk category, it is recommended that you explore options to address the potential risk.